## Slide 1
Virtual Kinetics Lab: Reaction Software
Thermochemical and Kinetic Parameters
Reaction Mechanism, pMuTT, pGrAdd
1
Online Workshop

## Slide 2: Agenda
Intro
Motivation
Link
Reaction Mechanism
Site vs State Model
Site model: Manual
Site model: Auto reaction mechanism generation
State model: Manual

## Slide 3: Agenda
Thermochemistry & Kinetics
Statistical thermodynamics overview
DFT to Macro Thermochemical Properties
Transition state theory (TST)
Reaction barriers
Pre-exponential factors
Python Multiscale Thermodynamic Toolbox (pMuTT)
Overview
Code demonstration
  Misc
    Re-referencing to standard state
    Lateral Interactions
    Empirical expressions

## Slide 4: Agenda
Semi-Empirical Methods
Group additivity
Bronsted-Evans-Polyani (BEP) Relationships
Linear Scaling Relationships (LSR)
Python Group Additivity (pGrAdd)
Code demonstration
Python Code Examples
DFTpMuTTopenMKM
Group addivity
Interesting applications (Error propagation & Dynamic catalysis)

## Slide 5: Introduction
Thermochemistry & Kinetics
Enthalpy, entropy, heat capacity
Reaction barriers
Pre-exponential factors
MKM input files
Reaction mechanism
Elementary reactions or States
Species
MKM Modeling Tool
Solve system of equations
Apply applicable constraints
Provide output
Post-modeling analysis
Time evolution
Reaction path analysis
Rate-limiting step
MARI/MASI
Reaction order
Apparent reaction barrier
Manual or RING
pMuTT, pGrAdd, BEP, LSR
openMKM
ReNView

## Slide 6: Reaction Mechanism: Site vs State Model
Site model
Active sites/Site density
Exclusion principle
Lateral interactions
Exhaustive elementary reactions
Mean-field
Ideal for typical heterogeneous catalysis
State model
Active sites/Site density
States vs sites
No interactions
States defined manually
Ideal for single atom and Zeolites

## Slide 7: Reaction Mechanism: Site Model
Simple reaction mechanism
1-2 Site types (Terrace vs step, Pt(111) & Pt(211))
Small molecules (CH4, NH3)
Manually generate all elementary reactions
Large reaction mechanism
>2 Site types
Large molecules
Automatic reaction mechanism generator (RING)

## Slide 8: Reaction Mechanism: Simple Site Model
Ammonia: 2 Ru active sites (Terrace & Step)
Summary
19 Reactions
3 Gas species
10 Surface species

## Slide 9: Reaction Mechanism: Large Site Model
Chemistry | System | Reactions (species)
Heterogeneous catalysis | Propane aromatization | 19907 (5909)
Gas phase combustion | Hexadecane combustion1 | 8130 (2116)
Metabolism | E.coli genome2 | 2077 (1039)
Metal chemistry | Glycerol decomposition3 | 3313 (537)
1 Combustion and Flame 2009, 156 (1), 181; 2 Mol Syst Biol. 2007, 3, 121; 3Green Chem., 2014,16, 813
Manual construction generally impractical
Automated network generators
  Generate all possible reactions and species of the network
  Use reaction rules as basis – “rule-based”

## Slide 10
Reaction network
List of species
List of reactions
Kinetic modeling
Network analysis
Semi-empirical analysis
1 Ind.Eng.Chem.Res. 1994, 33, 790; 2 AIChE Journal 2006, 52, 718; 3 Chemical Engineering Science 1992, 47, 2713; 4 J.Chem.Inf.Model. 2003, 43, 36;
5 Comp. Chem.Eng. 2008, 32, 2455; 6 Combustion & Flame, 2001, 126, 1780
RING
Initial reactants
Reaction rules
Reaction network generator can be used to construct the network

## Slide 11: Rule Input Network Generator (RING) for network generation
Domain specific English-like language using SILVER*
Reaction Language Compiler
Reaction Network Generator
Post-processing module
Reaction Network
Reactants
Reaction Rules
Initial reactants
System-specific rules
Inputs:
Reaction list
Species list
Cheminformatics Graph theory Graph transformation
Depth-first search Molecular hashing Subgraph extraction
Post-processing instructions

## Slide 12
User-specification
input reactant “C=CC”
input reactant “[{Zeo}H] ”
input reactant “N#N”
rule OlefinAdsorption{
gasPhase reactant r1{
C labeled c1
C labeled c2 double bond to c1}
reactant r2{
Zeo labeled z1 {! connected to >=1 C
with any bond}
H labeled h1 single bond to z1}
constraints{! r1 is cyclic}
form bond (c1,z1)
decrease bond order (c1,c2)
form bond (c2,h1)
break bond (z1,h1) }
RING language: rule inputs
REACTANTS
REACTION CENTER
c1
c2
z1
h1
Reaction
Center
CONSTRAINTS
TRANSFORMATIONS
Transformations
Final
configuration

## Slide 13: RING Ruleset: Typical hydrocarbon
rule CCScission{
reactant r1{
C labeled c1
C labeled c2 single bond to c1}
reactant r2{
Pt labeled m1{!connected to >0 $ with any bond}}
reactant r3 duplicates r2 (m1=>m2)
break single bond(c1, c2)
form single bond(c1, m1)
form single bond(c2, m2)}
rule CHScission{
reactant r1{
C labeled c1
H labeled h1 single bond to c1}
reactant r2{
Pt labeled m1{!connected to >0 $ with any bond}}
reactant r3 duplicates r2 (m1=>m2)
break single bond(c1, h1)
form single bond(c1, m1)
form single bond(h1, m2)
}
rule OHScission{
reactant r1{
O labeled o1
H labeled h1 single bond to o1}
reactant r2{
Pt labeled m1{!connected to >0 $ with any bond}}
reactant r3 duplicates r2 (m1=>m2)
break single bond(o1, h1)
form single bond(o1, m1)
form single bond(h1, m2)
}
input reactant "CCC"
input reactant "{Pt}"
define composite atom Pt
global constraints on Molecule{
fragment f1{
C labeled c1
C labeled c2 double bond to c1
Pt labeled p1 single bond to c1
}
fragment f2{
C labeled c1
C labeled c2 triple bond to c1
Pt labeled p1 single bond to c1
}
! Molecule contains >=1 of f1
! Molecule contains >= 1 of f2
}

## Slide 14: RING Ruleset: Output for CCC
Reactions (144) C(C)C.[{Pt}].[{Pt}]>>C([{Pt}])C.[{Pt}]C
C(C)C.[{Pt}].[{Pt}]>>C([{Pt}])(C)C.[{Pt}H]
C(C)C.[{Pt}].[{Pt}]>>C(C[{Pt}])C.[{Pt}H]
C([{Pt}])C.[{Pt}].[{Pt}]>>[{Pt}]C[{Pt}].[{Pt}]C
C([{Pt}])C.[{Pt}].[{Pt}]>>C([{Pt}])([{Pt}])C.[{Pt}H]
C([{Pt}])C.[{Pt}].[{Pt}]>>C(C[{Pt}])[{Pt}].[{Pt}H]
[{Pt}]C.[{Pt}].[{Pt}]>>[{Pt}]C[{Pt}].[{Pt}H]
C([{Pt}])(C)C.[{Pt}].[{Pt}]>>C([{Pt}])([{Pt}])C.[{Pt}]C
C([{Pt}])(C)C.[{Pt}].[{Pt}]>>C([{Pt}])([{Pt}])(C)C.[{Pt}H]
C([{Pt}])(C)C.[{Pt}].[{Pt}]>>C(C[{Pt}])([{Pt}])C.[{Pt}H]
C(C[{Pt}])C.[{Pt}].[{Pt}]>>C([{Pt}])C.[{Pt}]C[{Pt}]
C(C[{Pt}])C.[{Pt}].[{Pt}]>>C(C[{Pt}])[{Pt}].[{Pt}]C
C(C[{Pt}])C.[{Pt}].[{Pt}]>>C(C[{Pt}])([{Pt}])C.[{Pt}H]
Etc.
Species (55)
C(C)C 3 0
[{Pt}] 1 0
C([{Pt}])C 3 1
[{Pt}]C 2 1
C([{Pt}])(C)C 4 1
[{Pt}H] 1 1
C(C[{Pt}])C 4 1
[{Pt}]C[{Pt}] 3 2
C([{Pt}])([{Pt}])C 4 2
C(C[{Pt}])[{Pt}] 4 2
C([{Pt}])([{Pt}])(C)C 5 2
C(C[{Pt}])([{Pt}])C 5 2
C(CC)([{Pt}])[{Pt}] 5 2
C(CC[{Pt}])[{Pt}] 5 2
C([{Pt}])([{Pt}])[{Pt}] 4 3
C([{Pt}])([{Pt}])([{Pt}])C 5 3
C(C[{Pt}])([{Pt}])[{Pt}] 5 3
C=C 2 3
Etc.

## Slide 15: Reaction Mechanism: State Model
Reactions proceed from state to state
“Species” = States
Each state contains all the reactants or products
Limited to the proposed reaction paths…Might not be comprehensive
(1) Batchu, S. et.al.. Chem. 2023, 5 (1), 422–437.

## Slide 16: Statistical Thermodynamics
The collective body of statistical mechanics is based on two main postulates:
Equal a priori probability postulate
All microstates of the system of volume V that have the same energy and the same number of particles are equally probable
Ergodic hypothesis
The (long) time average of any mechanical property in a macroscopic system is equal to the average value of that property over all the microscopic states of the system, each weighted with its probability of occurrence, provided that the microscopic states replicate the thermodynamic state and environment of the actual system

## Slide 17: Statistical Thermodynamics: Partition functions and thermodynamic properties
For canonical ensemble

## Slide 18: Statistical Thermodynamics: Macro thermodynamic properties-Heat Capacity

## Slide 19: Statistical Thermodynamics: Macro thermodynamic properties-Enthalpy

## Slide 20: Statistical Thermodynamics: Macro thermodynamic properties-Entropy

## Slide 21: Transition State Theory: Reaction barrier and Pre-exponential factor
Initial State
Final State
Transition State
A + B
A --- B
AB
Ea
ERxn
Reaction Barrier
Pre-exponential factor
EIS
E‡
EFS

## Slide 22: Miscellaneous: Re-referencing
A
G
E
Experimental (NIST): STP
A*
B*
E*
F*
D*
C*
G*
DFT: Not STP
A*
B*
E*
F*
D*
C*
G*
DFT: STP
DFT derived thermochemistry is not at standard conditions
  Misstates energy
Need to atomistically adjust DFT derived thermochemistry to account for:
  Standard temperature
  Atomistic formation energies
  Error in DFT
Methods:
  Use know adsorption energies regressed to constituent atoms to shift DFT data
  Use DFT computed vs experimental thermochemistry for reference gases regressed to constituent atoms to shift DFT data

## Slide 23: Miscellaneous: Re-referencing
Name | NIST Enthalpy (kcal/mol)
CH4 | -17.89
CH3OH | -49.0
CH3CH3 | -20.0
CH2CH2 | 12.54
CH3CH2OH | -56.0
H2O | -57.798
CO2 | -94.051
H2 | 0.0
C
H
O
Apparent contribution to error per atom
Pseudo-inverse

## Slide 24: Miscellaneous: Lateral Interactions
Multiple species adsorbed on the surface of a heterogeneous catalyst can impact their energy
Some modeling tools (KMC) that track the position of all surface species provide multiple energies for all species based on 1st, 2nd, nth nearest neighbors.
Mean field model do not track exact adsorbate positions must rely on average surface coverages.
These corrections are often critical to model accuracy by not overstating adsorbate coverages.
These are expressed as the impact pairs of adsorbates have on each other using one or more linear relationships
I1
I2
I3
I4
I5
S1
S2
S3
S4

## Slide 25: Miscellaneous: Empirical Relationships
Simpler representation of thermodynamic property as function of temperature
Fitted using statistical thermodynamic or experimental data
Required by many material modeling programs
NASA Polynomials (7-coefficient)
Shomate Polynomials (NIST)
NASA Polynomials (9-coefficient)